## Slide 1: KLINGER FLUID CONTROL
Ball valve range KHI

## Slide 2: BALL VALVE range khi
Agenda
Overview product range KHI
New KHI “Industry” models:
KHI-F stainless steel construction
Dimensions
P/T diagrams
KHI-F/S carbon steel construction
Dimensions
P/T diagrams
Stem & O-Rings
Sealing elements
Trunnion & body seal
Certification, Kv values & torques
Top flange, gear/actuator sizing
Summary
Value selling
Classic KH(SV)I models:
KHI, KHSVI, KHSVI-VVS carbon steel construction
Dimensions
P/T diagrams
Stem & O-Rings
Sealing elements
Certification, Kv values & torques
Top flange, gear/actuator sizing
Value selling

## Slide 3: overview
Product range
KHI-F stainless steel DN150 - 400
KHI-F carbon steel DN150 - 400
KHI-S carbon steel DN150 - 400
KHI carbon steel DN500 - 800
KHSVI carbon steel DN500 - 1000
KHSVI VVS carbon steel DN150 - 800
New KHI „Industry“ models
Classic KH(SV) models

## Slide 4: New khi „industry“ models
DN150 – 400 carbon & stainless steel
KHI-F stainless steel DN150 - 400
KHI-F carbon steel DN150 - 400
KHI-S carbon steel DN150 - 400

## Slide 5: KHI-F, stainless steel
Construction DN150 - 400

## Slide 6: KHI-F stainless steel
Dimensions DN150 - 400
PN40 PN25 PN16 PN10 Cl300 Cl150
+
Face to face dimensions:
PN10/16/25/CL150 acc. EN558-1 row 12 / ANSI B16.10 long pattern
PN40/CL300 acc. EN558-1 row 4 / ANSI B16.10 long pattern
Connection flanges:
Acc. EN1092-1 for PN10/16/25/40
Acc. ANSI B16.5 for CL150/300

## Slide 7: P/T diagrams
KHI-F, stainless steel

## Slide 8: P/T diagrams
KHI-F, duplex

## Slide 9: KHI-F, carbon steel
Construction DN150 - 400

## Slide 10: KHI-F carbon steel
Dimensions DN150 - 400
PN40 PN25 PN16 PN10 Cl300 Cl150
+
Face to face dimensions:
PN10/16/25/CL150 acc. EN558-1 row 12 / ANSI B16.10 long pattern
PN40/CL300 acc. EN558-1 row 4 / ANSI B16.10 long pattern
Connection flanges:
Acc. EN1092-1 for PN10/16/25/40
Acc. ANSI B16.5 for CL150/300

## Slide 11: P/T diagrams
KHI-F, carbon steel

## Slide 12: KHI-S, carbon steel
Construction DN150 - 400

## Slide 13: KHI-S carbon steel
Dimensions DN150 - 400

## Slide 14: P/T diagrams
KHI-S, carbon steel

## Slide 15: KHI-F/S
Top Flange acc. to ISO 5211: for direct connection to gearbox or bridge
Graphite sealing  Fire Safe acc. ISO 10497 & API 607 in standard version
Stem O-rings in different versions:
A75H (FEPM) standard -10°C to +250°C
V71C (FEPM) low temperature -45°C to +200°C
C70M for ammonia -30°C to +125°C
EN682 (FKM) gas version 0°C to +150°C
(4) One large bearing bush: Stainless steel /PTFE or 1.4462 / PTFE
(5) Back up ring KFC
Stem and O-Rings
Flange plate
Stem
Body
1
2
3
4
5
Stem/shaft

## Slide 16: KHI-F/S
Wire Ring
Screw
Support Ring
Sealing Ring
Standard KFC
On Demand METAL
U – Sleeve and O-Ring (Back-up Sealing)
The sealing system at the ball is pre-stressed during assembly. The two pre-stressed elastic sealing elements made of stainless steel and featuring sealing rings and a back seal (consisting of a U-sleeve and an O-ring) form a system upstream and downstream of the valve together with the ball. Furthermore, a support ring protects the elastic sealing element against overloads, for example caused by water hammers. A wire ring safeguards the sealing unit.
The ball valve can be pressurized in both flow directions. The elasticity of the sealing elements allows for a compensation of thermal expansion. Thanks to this function, two primary sealed areas are constantly present in the bore.
Sealing elements

## Slide 17: Khi-f/S
Friction washer PEEK
O-Ring for better leak proof
Distance washer 1.4404 / 316L
C4430 gasket  Fire safe acc. ISO10497 & API607 and fugitive emission ISO15848-1
Lock washer (Nordlock) 1.4404 /316L - no loosen because of vibration
Trunnion
Bearing pin
Bearing plug
Hex headscrew
1
2
3
4
5
Screws A4-70 instead of stud & nut
Added C4430 sealing
  Firesafe acc. ISO 10497 & API 607and fugitive emission acc. ISO15848-1
O-Ring as radial sealing
  better handling & leak proofness
1
2
3
Division flange and sealing

## Slide 18: Khi-f/S
Certification, Kv vales & torques
KV VALUES
MAST 20°C, Nm
TORQUES KFC SEATS
TORQUES METAL SEATS
FIRE SAFE : The ball valve can be used for fire-safe applications and is certified in accordance with API Standard 607 and EN ISO 10497.
DBB : With the DBB function you only need one KLINGER Ballostar KHI-F ball valve instead of two separate valves. This alternative solution either with a test and drain valve not only saves time and money but is especially useful for installations with limited space.
ISO15848-1 : The KLINGER Ballostar KHI-F is significantly below prescribed emission limits for keeping air clean. Certified emission testing to ISO 15848-1 (fugitive emissions), ISO FE CH-C03-SSA0-tRT (120°C) and fulfill TA-Luft.
O2 : The Ballostar KHI ball valve series are useable for applications with gaseous oxygen at operating pressures of up to 16 bar for carbon steel, up to 30 bar for stainless steel and operating temperatures of up to 60 °C.
EN12266-1 : The KHI-F ball valves with KFC sealing elements fulfill the leakage rate A acc. to EN 12266-1/ISO 5208 soft seated and leakage rate Class IV-S1 acc. to EN 60534-4 metal seated.

## Slide 19: TOP flange
ISO 5211
Square end, optional feather key
ISO TOP flange acc. ISO 5211
Size | PN | Square | Feather key | ISO5211 soft seat | ISO5211 metal seat
DN150 | 10/16/25/CL150 | SW36 | 48 | F14 | F14
DN200 |  | SW36 | 48 | F14 | F14
DN250 |  | SW46 | 60 | F16 | F16
DN300 |  | SW55 | 72 | F25 | F25
DN350 |  | SW55 | 72 | F25 | F30
DN400 |  | SW55 | 72 | F25 | F30
Size | PN | Square | Feather key | ISO5211 soft seat | ISO5211 metal seat
DN150 | 40/CL300 | SW36 | 48 | F14 | F14
DN200 |  | SW36 | 48 | F14 | F16
DN250 |  | SW46 | 60 | F16 | 25
DN300 |  | SW55 | 72 | F25 | F25
DN350 |  | SW55 | 72 | F25 | F30
DN400 |  | SW55 | 72 | F25 | F30

## Slide 20: Gear sizing auma
GS gears with hand wheel
Size | PN | ISO5211 soft seat | Gear type soft seat | ISO5211 metal seat | Gear type metal seat
DN150 | 10/16/25/CL150 | F14 | GS 80.3-53:1 | F14 | GS 80.3-53:1
DN200 |  | F14 | GS 80.3-53:1 | F14 | GS 80.3-53:1
DN250 |  | F16 | GS 100.3-208:1 | F16 | GS 100.3-208:1
DN300 |  | F25 | GS 125.3-208:1 | F25 | GS 125.3-208:1
DN350 |  | F25 | GS 125.3-208:1 | F30 | GS160.3-(442:1)
DN400 |  | F25 | GS 125.3-208:1 | F30 | GS160.3-(442:1)
Size | PN | ISO5211 soft seat | Gear type soft seat | ISO5211 metal seat | Gear type metal seat
DN150 | 40/CL300 | F14 | GS 80.3-53:1 | F14 | GS 80.3-53:1
DN200 |  | F14 | GS 80.3-53:1 | F16 | GS 100.3-208:1
DN250 |  | F16 | GS 100.3-208:1 | 25 | GS 125.3-208:1
DN300 |  | F25 | GS 125.3-208:1 | F25 | GS 125.3-208:1
DN350 |  | F25 | GS 125.3-208:1 | F30 | GS160.3-(442:1)
DN400 |  | F25 | GS 125.3-208:1 | F30 | GS160.3-(442:1)
AUMA coupling
AUMA gear
ISO TOP flange

## Slide 21: Actuator sizing auma
“SA” actuators
Size | PN | Soft seat | Actuator type soft seat | Metal seat | Actuator type metal seat
DN150 | 10/16/25/CL150 | F14 | GS 80.3-F14 (53:1) SA07.6 | F14 | GS 80.3-F14 (53:1) SA10.2
DN200 |  | F14 | GS 80.3-F14 (53:1) SA07.6 | F14 | GS 80.3-F14 (53:1) SA10.2
DN250 |  | F16 | GS 100.3-F16 (208:1) SA07.6 | F16 | GS 100.3-F16 (208:1) SA07.6
DN300 |  | F25 | GS 125.3-F25 (208:1) SA07.6 | F25 | GS 125.3-F25 (208:1) SA10.2
DN350 |  | F25 | GS 125.3-F25 (208:1) SA10.2 | F30 | GS160.3-F30 (442:1) SA07.6
DN400 |  | F25 | GS 125.3-F25 (208:1) SA10.2 | F30 | GS160.3-F30 (442:1) SA10.2
DN150 | 40/ CL300 | F14 | GS 80.3-F14 (53:1) SA10.2 | F14 | GS 80.3-F14 (53:1) SA10.2
DN200 |  | F14 | GS 80.3-F14 (53:1) SA10.2 | F16 | GS 100.3-F16(208:1) SA07.6
DN250 |  | F16 | GS 100.3-F16 (208:1) SA07.6 | F25 | GS 125.3-F25 (208:1) SA10.2
DN300 |  | F25 | GS 125.3-F25 (208:1) SA10.2 | F25 | GS160.3-F25 (442:1) SA07.6
DN350 |  | F25 | GS 125.3-F25 (208:1) SA10.2 | F30 | GS160.3-F30 (442:1) SA10.2
DN400 |  | F25 | GS 125.3-F25 (208:1) SA10.2 | F30 | GS160.3-F30 (442:1) SA10.2
AUMA coupling
ISO TOP flange
AUMA gear
AUMA actuator

## Slide 22: Actuator sizing pneumatic
Size | PN | Air supply for actuator min. 5 bar |  |  | 
 |  | SA soft seat | DA soft seat | SA metal seat | DA metal seat
DN150 | 10/16/25/CL150 | AT651U-S10-F16/SW46 | AT551U-DA-F14/SW36 | AT751U-S10-F16/SW46 | AT651U-DA-F16/SW46
DN200 |  | AT701U-S10-F16/SW46 | AT651U-DA-F16/SW46 | AT751U-S10-F16/SW46 | AT651U-DA-F16/SW46
DN250 |  | AT751U-S10-F16/SW46 | AT701U-DA-F16/SW46 | AT1001U-S10-F25/SW55 | AT751U-DA-F16/SW46
DN300 |  | AT1001U-S10-F25/SW55 | AT801U-DA-F25/SW55 | n.a. | AT1001U-DA-F25/SW55
DN350 |  | n.a. | AT1001U-DA-F25/SW55 | n.a. | n.a.
DN400 |  | n.a. | AT1001U-DA-F25/SW55 | n.a. | n.a.
Air Torque
DN150 | 40/ CL300 | AT751U-S10-F16/SW46 | AT651U-DA-F16/SW46 | AT751U-S10-F16/SW46 | AT651U-DA-F16/SW46
DN200 |  | AT751U-S10-F16/SW46 | AT651U-DA-F16/SW46 | AT801U-S10-F16/SW46 | AT701U-DA-F16/SW36
DN250 |  | AT1001U-S10-F25/SW55 | AT751U-DA-F16/SW46 | AT1001U-S10-F25/SW55 | AT1001U-DA-F25/SW46
DN300 |  | n.a. | AT1001U-DA-F25/SW55 | n.a. | AT1001U-DA-F25/SW55
DN350 |  | n.a. | AT1001U-DA-F25/SW55 | n.a. | n.a.
DN400 |  | n.a. | AT1001U-DA-F25/SW55 | n.a. | n.a.
Bracket & coupling
ISO TOP flange
Pneum. actuator
Switch box & solenoid valve

## Slide 23: summary
(1) Fugitive emissions acc. to ISO 15848-1 due to added C4430 gasket on trunnion and division flange (optimized trunnion and division flange construction)
(2) Fire safe acc. ISO10497 & API607 in standard version due to added graphite sealing on stem
(3) Max. temperature: +250°C due to optimized O-Ring construction on stem
(4) EN12266-1 (ISO5208) P12 leakage rate A for soft seated, leakage rate IV-S1 acc. to EN 60534-4 for metal seat due to reliable sealing system
(5) Weight optimized ball and body casting (investment, replicast)
Body material stainless steel 1.4581 or duplex 1.4470
(6) Top Flange acc. to ISO 5211: for direct connection to gearbox or bridge
PED 2014/68/EU (pressure equipment directive)
Double Block & Bleed acc. ISO 5208 and ISO 14313
SIL Level: SIL 2 (reliability)
BAM Oxygen (material test for oxygen)
Features
1
1
2
3
4
6
5
5

## Slide 24: Value selling
KHI-F | KEY FEATURES | USP | CUSTOMER VALUE | BENEFIT
 | Different types of shaft O-rings depending on the process. Soft and metal sealing elements. | Excellent adaptation to the application and various processes. Valid for corrosive/abrasive media and high operating cycles. High standard temperature range. Sealing elements are insensitive to solids. | One-stop solution for various situations in different industries. | Maximum flexibility and adaptability. Standard version leakage rate A. No blocking of the sealing elements due to impurities.
 | Body and ball construction. Body materials: 1.4581, duplex | Weight-optimised, casted housing and ball. When metal seats are used, the ball is chrome coated. | The robust casted housing and ball are insensitive to pressure shocks and thermal influences. Due to weight optimisation, easy handling during installation is ensured. The chrome layer ensures max. hardness and min. surface roughness  no sticking particles | Sustainable, durable and highly available ball valve construction. Time savings during installation due to low weight. High service life of the seats when the ball is chrome coated.
 | Double block & bleed version | Drain/test valve available for all line sizes. | Possibility of draining the cavity and tightness check of the upstream sealing element. | Maximum plant safety and security during maintenance work.
 | Maintenance | Simple parts – easy to maintain. | Easy handling due to simple construction. | Saving effort and time for maintenance.
 | Service Life | High-quality parts and good workmanship. | Durable product when correctly designed and spare parts are readily available. | Cost savings through long service life and shorter maintenance cycles.
 | Certification | Fire Safe acc. EN10497/API 607 and ISO15848-1 certification in standard version (Gas certificate and oxygen BAM approval available). | Fire safe and Emissions Certification (ISO15848) in one construction. | High availability in case of ignition of the media and increased tightness to atmosphere.
 | Standard and special applications | Customised solutions for critical media/applications. Ideally suited also for standard applications. | Regardless of the application, a ball valve solution is always available. | Maximum coverage of requirements with one ball valve model.
KHI-S/F, DN150 – DN400

## Slide 25: Classic kh(SV)I models
KHI, KHSVI, KHSVI VVS
KHI carbon steel DN500 - 800
KHSVI carbon steel DN500 - 1000
KHSVI VVS carbon steel DN150 - 800

## Slide 26: construction
KHI, KHSVI, KHSVI-VVS
Ball, chromed
Stem SS
Bearing bush
Bush insert
Stem O-Rings
Washer
Flange plate & screws
Body seal
Trunnion, soft nickle gasket
Body
Drain valve
Sealing element
Body end piece
KHI carbon steel DN500 - 800
KHSVI carbon steel DN500 - 1000
KHSVI-VVS carbon steel DN150 - 800
 | Execution | Hardness | Surface roughness (RZ)
 | Ductile graphite iron ball chrome plated | 800 – 1000 HV | 0,6 µm
Competitor | Nickel plated | 500 – 650 HV | 5,6 µm
 | Stainless steel | 300 – 350 HV | 3,5 µm

## Slide 27: dimensions
KHI
KHI full bore:
DN500 to DN800, PN25/40
Face to face length acc EN558-1, size 12, flanges acc. EN1092-1
Body material 1.0619
Standard temperature Version 0°C to +200°C, Low Temperature Version -45°C to +200°C
Ball EN-JS1030Fe/Cr30f,mt/ 1.4408 trunnion mounted, stem 1.4104
Painting carbon steel body:
Material VIII Sky blue RAL 5015

## Slide 28: dimensions
KHSVI
KHSVI full bore:
DN500 to DN1000, PN25/40
Face to face length acc EN12982 size 63 / ANSI B16.10 Cl300, Body material 1.0619
Weld end dimensions on demand
Standard temperature Version 0°C to +200°C, Low Temperature Version -45°C to +200°C
Ball EN-JS1030Fe/Cr30f,mt/ 1.4408 trunnion mounted, stem 1.4104
Painting carbon steel body:
Material VIII Sky blue RAL 5015

## Slide 29: dimensions
KHSVI-VVS
KHSVI – VVS fully welded full bore
DN150 to DN800, PN25/40, Body material 1.0619
DN150 – 250 F/F length acc EN12982 size 61
DN300 – 800 F/F length acc EN12982 size 63 / ANSI B16.10 Cl300
Certified acc. EN488:2019, EHP003
Standard temperature Version 0°C to +250°C, Low Temperature Version -45°C to +200°C
Ball EN-JS1030Fe/Cr30f,mt/ 1.4408, trunnion mounted, stem 1.4104
Painting carbon steel body:
Material VIII Sky blue RAL 5015
DN150-250
DN300-800

## Slide 30: P/T diagrams
KHSVI-VVS:
KHI, KHSVI:
KHI, KHSVI, KHSVI-VVS, carbon steel

## Slide 31: Stem o-rings
Standard O-Rings AFLAS
Temperature Range 0°C to 200°C
Low Temperature O-Rings V71C :
Temperature Range -45°C to 200°C,
Gas O-Rings FPM
Temperature Range 0°C to 150°C
KHI, KHSVI, KHSVI-VVS

## Slide 32: Sealing elements
Wire Ring
Screw
Support Ring
Sealing Ring
Standard KFC
On Demand METAL
U – Sleeve and O-Ring (Back-up Sealing)
The sealing system at the ball is pre-stressed during assembly. The two pre-stressed elastic sealing elements made of stainless steel and featuring sealing rings and a back seal (consisting of a U-sleeve and an O-ring) form a system upstream and downstream of the valve together with the ball. Furthermore, a support ring protects the elastic sealing element against overloads, for example caused by water hammers. A wire ring safeguards the sealing unit.
The ball valve can be pressurized in both flow directions. The elasticity of the sealing elements allows for a compensation of thermal expansion. Thanks to this function, two primary sealed areas are constantly present in the bore.
KHI, KHSVI, KHSVI-VVS

## Slide 33: Detail sealing element

## Slide 34: DBB function

## Slide 35: certifiction
KHI, KHSVI, KHSVI-VVS, Kv values & torques
FIRE SAFE : The Fire Safe tests in accordance with API Standard 607, 4th Edition and EN ISO 10497:2004 have been certified by Lloyd's Register and TÜV Austria respectively.
DBB : The KLINGER Ballostar® KHI represents a safe shut-off for the operation of steam boilers in the sense of item 6231 TRD 601 B12.
GAS APPROVAL : ÖVGW Certificate for authorization to display the ÖVGW quality label "Gas" for the ball valves GKHI, GKHSVI and GKHSVI VVS, DN 150 - 800.
O2 : The BAM Berlin has granted its approval for the ball valve series Ballostar® KHI in utilization scenarios with gaseous oxygen at operating pressures of up to 16 bar and operating temperatures of up to 60 °C.
VDI 2440 : Certified emission testing pursuant to VDI 2440 for Ballostar® KHI / KHSVI ball valves at temperatures < 250 °C.
EN488:2019 KHSVI VVS : KLINGER Ballostar® KHSVI VVS ball valves, DN 150 to 800, have been successfully tested and certified by the TÜV Austria under inclusion of the extended requirements of the EN 488:2019.
TORQUES KFC SEATS
KV VALUES

## Slide 36: Top flange
DN150 & 200
DN250 - 1000
Connection Flange F10, F12, F14, F16
Square end SW32
Feather Key
Connection Plate
DN250, 300: F16/F25
DN350, 400: F25
DN500, 600: F25/F30
DN700, 800: F35
DN1000: F40/F48
Plug-in coupling with serration and feather key for AUMA gears
GS60.3
GS80.3
SW27
SW36
SW46
SQ10.2
Dia. 36
EN ISO 5211

## Slide 37: Ball valve kh(sv)I
AUMA basic configuration
(1) Stem of KH(SV)I with feather key (DN250 to 1000). DN150 and DN200 with square end.
(2) Connection plate acc. ISO5211 (line size 250 to 1000) to connect gear with valve. F size of connection plate and actuator must match. For sizes DN150 and 200 a connection flange in different F Sizes will be used.
(3) Plug-in coupling with serration and feather key connection.
(4) Mech. gear AUMA type “GS”
(5) El. Mech. Actuator AUMA type “SA”, “SAR” or “SAExC”.
(6) Actuator control AUMA type “AM” or “AC”.
(7) Complete AUMA unit: mech. Gear + actuator + actuator control
1
2
3
4
5
6
7

## Slide 38: Gear sizing AUMA
PN25
AUMA gear sizing hand operation KH(SV)I PN25-KFC |  |  |  |  | 
Size | Nm valve | Nm gear | Gear type | ISO5211 | Hand wheel (dm)
DN150 | 651 | 1000 | GS 63.3-51:1/H | F12 | 315
DN200 | 1069 | 2000 | GS 80.3-53:1/H | F14 | 400
DN250 | 2083 | 4000 | GS 100.3-208:1/H | F16 | 315
DN300 | 3710 | 4000 | GS 100.3-208:1/H | F16 | 315
DN350 | 5068 | 8000 | GS 125.3-208:1/H | F25 | 400
DN400 | 6251 | 8000 | GS 125.3-208:1/H | F25 | 400
DN500 | 8701 | 14000 | GS 160.3-442:1/H | F25 | 400
DN600 | 13020 | 28000 | GS 200.3-434:1/H | F30 | 630
DN700 | 19320 | 28000 | GS 200.3-434:1/H | F35 | 630
DN800 | 31395 | 56000 | GS 250.3-411:1/H | F35 | 630
DN1000 | 45000 | 90000 | GS 315/GZ30.1-16 | F40 | 630

## Slide 39: Actuator sizing AUMA
PN25
AUMA gear & actuator sizing motor operation KH(SV)I PN25-KFC |  |  |  |  |  |  | 
Size | Nm valve | Nm gear | Gear type | ISO5211 | Actuator type | Closing time (sec.) | RPM
DN150 | 651 | 800 | GS 63.3-51:1/H | F12 | SA 07.6 | 35 | 22
DN200 | 1069 | 1600 | GS 80.3-53:1/H | F14 | SA 10.2 | 50 | 16
DN250 | 2083 | 3200 | GS 100.3-208:1/H | F16 | SA 07.6 | 69 | 45
DN300 | 3710 | 6400 | GS 125.3-208:1/H | F25 | SA 07.6 | 98 | 32
DN350 | 5068 | 6400 | GS 125.3-208:1/H | F25 | SA 10.2 | 98 | 32
DN400 | 6251 | 11200 | GS 160.3-442:1/H | F25 | SA07.6 | 147 | 45
DN500 | 8701 | 11200 | GS 160.3-442:1/H | F25 | SA 10.2 | 147 | 45
DN600 | 13020 | 22400 | GS 200.3-864:1/H | F30 | SA 10.2 | 206 | 63
DN700 | 19320 | 22400 | GS 200.3-864:1/H | F35 | SA 10.2 | 288 | 45
DN800 | 31395 | 44800 | GS 250.3-848:1/H | F35 | SA 14.2 | 283 | 45
DN1000 | 45000 | 63000 | GS 315/GZ30.1-16 | F40 | SA14.2 | 283 | 45

## Slide 40: Gear sizing auma
PN40
AUMA gear sizing hand operation KH(SV)I PN40-KFC |  |  |  |  | 
Size | Nm valve | Nm gear | Gear type | ISO5211 | Hand wheel (dm)
DN150 | 1260 | 2000 | GS 80.3-53:1/H | F14 | 400
DN200 | 1757 | 2000 | GS 80.3-53:1/H | F14 | 400
DN250 | 2905 | 4000 | GS 100.3-208:1/H | F16 | 315
DN300 | 5733 | 8000 | GS 125.3-208:1/H | F25 | 400
DN350 | 7063 | 8000 | GS 125.3-208:1/H | F25 | 400
DN400 | 7987 | 14000 | GS 160.3-442:1/H | F25 | 400
DN500 | 11655 | 28000 | GS 200.3-434:1/H | F30 | 630
DN600 | 15540 | 28000 | GS 200.3-434:1/H | F30 | 630
DN700 | 27510 | 56000 | GS 250.3-411:1/H | F35 | 630
DN800 | 36960 | 56000 | GS 250.3-411:1/H | F35 | 630
DN1000 | 60000 | 90000 | GS 315/GZ30.1-16 | F40 | 630

## Slide 41: Actuator sizing AUMA
PN40
AUMA gear & actuator sizing motor operation KH(SV)I PN40-KFC |  |  |  |  |  |  | 
Size | Nm valve | Nm gear | Gear type | ISO5211 | Actuator type | Closing time (sec.) | RPM
DN150 | 1260 | 1600 | GS 80.3-53:1/H | F14 | SA 10.2 | 36 | 22
DN200 | 1757 | 3200 | GS 100.3-208:1/H | F16 | SA 07.6 | 50 | 63
DN250 | 2905 | 6400 | GS 125.3-208:1/H | F25 | SA07.6 | 69 | 45
DN300 | 5733 | 11200 | GS 160.3-442:1/H | F25 | SA07.6 | 105 | 63
DN350 | 7063 | 11200 | GS 160.3-442:1/H | F25 | SA07.6 | 105 | 63
DN400 | 7987 | 11200 | GS 160.3-442:1/H | F25 | SA 10.2 | 147 | 45
DN500 | 11655 | 22400 | GS 200.3-864:1/H | F30 | SA07.6 | 144 | 90
DN600 | 15540 | 22400 | GS 200.3-864:1/H | F30 | SA 10.2 | 206 | 63
DN700 | 27510 | 44800 | GS 250.3-848:1/H | F35 | SA10.2 | 283 | 45
DN800 | 36960 | 44800 | GS 250.3-848:1/H | F35 | SA 14.2 | 283 | 45
DN1000 | 60000 | 125000 | GS 400/GZ35.1-16 | F48 | SA14.6 | 288 | 45

## Slide 42: Value selling
KH(SV)I | KEY FEATURES | USP | CUSTOMER VALUE | BENEFIT
 | Different types of shaft O-rings depending on the process. Soft and metal sealing elements. | Excellent adaptation to the application and various processes. Valid for corrosive/abrasive media and high operating cycles. High standard temperature range. Sealing elements are insensitive to solids. | One-stop solution for various situations in different industries. | Maximum flexibility and adaptability. Standard version leakage rate A. No blocking of the sealing elements due to impurities.
 | Body and ball construction. Body material: 1.0619 Fully welded version | Robust casted housing and ball. When metal seats are used, the ball is chrome coated. Fully welded version for underground applications – only one welding seam in flow direction | The robust casted housing and ball are insensitive to pressure shocks and thermal expansion. The chrome layer ensures max. hardness and min. surface roughness  no sticking particles. Fully welded version ensures max. resilience against tension, compression and bending forces. | Sustainable, durable and highly available ball valve construction. High service life of the seats when the ball is chrome coated. EN488:2019 certification for the fully welded version.
 | Double block & bleed version | Drain/test valve available for all line sizes. | Possibility of draining the cavity and tightness check of the upstream sealing element. | Maximum plant safety and security during maintenance work.
 | Maintenance | Simple parts – easy to maintain. | Easy handling due to simple construction. | Saving effort and time for maintenance.
 | Service Life | High-quality parts and good workmanship. | Durable product when correctly designed and spare parts are readily available. | Cost savings through long service life and shorter maintenance cycles.
 | Certification | Fire Safe acc. EN10497/API 607, TA Luft, Gas, oxygen BAM approval and EN488:2019 for fully welded version. | High range of available certificates. | Suitable for many different application
 | Standard and special applications | Customised solutions for critical media/applications. Ideally suited also for standard applications. | Regardless of the application, a ball valve solution is always available. | Maximum coverage of requirements with one ball valve model.
KH(SV)I, DN500 – DN1000

## Slide 43
KLINGER Fluid Control GmbH
Am Kanal 8-10 » A-2352 Gumpoldskirchen
T +43 2252 600 100
office@klinger.kfc.at
THANKS FOR YOUR ATTENTION!